## Slide 1: Physical networks

## Slide 2
Now that we have spent several weeks on the software that makes networks tick. Lets spend some time looking at physical networks!

## Slide 3: Network Topology

## Slide 4: What is Topology?
Topology
The arrangement and interlinking of computers in a computer network
dictionary.com

## Slide 5: Factors of a topology
Cost
Flexibility
Reliability
Scalability
Ease of installation
Ease of maintenance.

## Slide 6: Bus Topology
Data travels in both directions along the bus
All devices are connected to the bus
When device wants to transmit packet, destination address has to be included in the header.
Advantages
  Easy to install
  Can be extended easily
  Very reliable because of single transition line
Disadvantages
  Troubleshooting is difficult as there is not single point of control
  One faulty node can being the while network down
  Dumb terminals cannot be connected to the bus

## Slide 7: Ring Topology
Each node is connected to exactly 2 other nodes
Data travels in one, predetermined, direction
Only one token allowed
Sender submits a packet
  Neighbouring node transmits it to its neighbour and so on
  Eventually, packet reaches the destination and is removed
  Or
  Packet reaches sender and is removed.
Advantages
  Small cable segments
  Ideal for optical fibre as data travels in only one direction
  Very high transition speeds possible.
Disadvantages
  Failure of single node brings down the whole network
  Troubleshooting is difficult as many nodes may have to be inspected before problem is identified.
  Difficult to remove one or more nodes while keeping the network operational.

## Slide 9: Star Topology
Server
All Nodes are connected to central server
Server is responsible for passing on all communications
Possibly the most common topology
Advantages
  Failure a node dose not affect the network
  Trouble shooting is easy as faulty node can be detected from central point
  Simple access protocols required as one of the communicating nodes is always the server.
Disadvantages
  Longer cables to connect to server
  Failure of central node brings whole network down.

## Slide 10: Tree Topology
Combination of star and bus topologies
Groups of star networks connected with a bus backbone
Advantages
  Existing networks can be easily expanded
  Point-to-point wiring for individual segments means easier installation and maintenance
  Well suited for temporary networks
Disadvantages
  Technical experience required to configure and wire tree
  Failure of backbone brings down entire network
  Maintenance difficult for large networks

## Slide 11: Transmission Media

## Slide 12
Guided
  Transmitted data travels through cables and along known, fixed paths.
Unguided
  Transmitted data travels through space in the form of electromagnetic waves.

## Slide 13: Twisted Pair Cable
Shielded and unshielded
Most common type of network cable
Supports 100 base T and 1000 base T (100 mb/s, 1000mb/s)
Twisted to reduce noise on the line from magnetic fields
Notes: Most common type of data cable
Found in most networks. Its in this room, my house, probably your house (if you wired your computers to your modem).
4 sets to twisted wires. Twisted to reduce noise on the line from magnetic fields.
STOP! Physics time!
Magnetic fields are generated when electrons flow through circet.
They follow the “left hand rule”. Magnetic fields rotate clockwise as electrons flow away from you.
If you have 2 fields, next to each other, rotating clockwise and counter clockwise, then the net field has a direction away from the cable.
If another magnetic field comes along (imagine a magnet) then its field affects the field of the cable but only in one location. This move the magnet around a bit and you can artificially drag the data line high and low. This would affect the data we are passing and mess up our data. Not what we want.
How ever if we twist the wires around each other, we end up with alternating magnetic fields all the way along the cable.
Now when we move the magnet, we pall the line high in one location but pull it low in the another location (depending on the twist). The high is the invers of the low and the to cancel out, leaving us with just our data…. Electrical engineers are smart buggers 
Cat5e and cat6 comes with more shielding to help further reduce interference. It always reminded me if tinfoil.
But, for all its graces, Cat5, 5e and 6 are a nightmare to wire yourself.

## Slide 14: UTP/STP
Cat5 = 100 mb/s
Cat5e = 1000 mb/s
Cat6 = 10,000 mb/s
these are the theoretical maximum speeds and distance please a factor. In more situations, you should get reasonable close to these numbers.

## Slide 15: Coaxial Cable
10 baseT = 10mb/s

## Slide 16: Optical
Advantages
  Fast, really fast
Disadvantages
  Expensive
  Easy to break

## Slide 17: Hardware

## Slide 18: Computer
We all know what these things are
Sometime there consumer grade
Some times there servers

## Slide 19: Hubs
Operates at layer 1 of the OSI model
Can support 10 to 1000 mb/s
Largely obsolete
Can cause packet collisions as hubs send packets to all connected device.

## Slide 20: switches
Notice a difference?
  You can be forgiven if you cant
Switches are almost the same as hubs
More intelligent as they send packets to the correct device, based on mac address
More common that hubs now

## Slide 21: Router
Network device that forwards packets between networks.
Can have switch built in but not necessary
May include firewall, VPN

## Slide 22: The Cloud
Not hardware
It’s a general idea of things that exist on the internet.
Its just servers
And services
IT IS NOT THE ANSWER!

## Slide 23: Questions?